## Slide 1: SIMPLIS Simulation Analysis & Control Functions
POP Analysis (v9.20)
  Pre-POP Transient (v9.30)
  N-cycles before launching POP
  Core POP Process
Transient Analysis (v9.20)
Matt Fortin and Tom Wilson
18 Sept 2025

## Slide 2: SIMPLIS – Simulation Analysis & Control Functions
Analysis Type Source
Early Stop of Pre-POP Transient
Early Start of Saving Data
Early Stop of Transient
18 Sept 2025

## Slide 3: Please check out our SIMPLIS Essentials Online Short Course
We cannot review here all the critical aspects of how POP works
Everything you need to know about
  How POP works, and
  How to set up POP, AC and Transient analyses
  is covered in our SIMPLIS Essentials Online Short Course
  https://www.simplistechnologies.com/training/simplis-essentials
Accessible from our home page
https://simplis.com/
18 Sept 2025

## Slide 4: Example 1: Illustrate operation of Analysis Type Source
Analysis Type Source
Use LLC Converter to illustrate basic functionality of Analysis Type Sources
Show GUI for each source
Run ckt
Go over waveforms
18 Sept 2025

## Slide 5
Analysis Type Source
Use POP Analysis and AC Analysis Sources to Enable and Disable portions of the control circuit (e.g. a Dithering control feature)
  Note: Dither circuit defeats POP
    Step 1  Create Dither feature
    Step 2  Enable/Disable Dither feature
    Step 3  Use POP & AC Analysis Sources to Enable/Disable Dither feature
    Step 4  Add LISN to examine Dither feature performance
      Note: Dither circuit does its job
Example 2: Use Simulation Analysis & Control Functions to Enable/Disable portions of Controller Circuit
18 Sept 2025

## Slide 6
Window Detector
  Detects when input vIN is
    Less than VREF1, and
    Greater than VREF2
    For at least a DwellTime = 10us
  Outputs a trigger_OUT signal of pulse width = 50ns
Connect output of Window Detector to
Early Stop of Pre-POP Transient
  Pre-POP Transient is halted by either a
  Trigger_OUT signal from the Window
  Detector or the specified max duration of the Pre-POP Transient
Example 3: Use Window Detector to Trigger
Early Stop of Pre-POP Transient
18 Sept 2025

## Slide 7
Window Detector
  Detects when input vIN is
    Less than VREF1, and
    Greater than VREF2
    For at least a DwellTime = 10us
  Outputs a trigger_OUT signal of pulse width = 50ns
Output of Detector initiates Early Start of Saving Data, and after fixed delay, Early Stop of Transient
Example 4: Use Window Detector to Trigger
Early Start of Saving Data & Early Stop of Transient
18 Sept 2025

## Slide 8
All Early Start or Early Stop features need to be Enabled
POP Advanced Options
There is rarely any reason not to check
“Enable Auto Max Period”
Pre-POP Transient
18 Sept 2025

## Slide 9
All Early Start or Early Stop features need to be Enabled
Transient Advanced Options
18 Sept 2025

## Slide 10: Observations
These tools can help you better understand
  Your circuit, and
  How POP is interacting with your circuit
You can use these tools to find a good POP initialization strategy
NOTE: Craft your detection circuits carefully
  Minimize the number of new topologies that they introduce
  NOTE: the Window Detector used here introduces zero new topologies
18 Sept 2025

## Slide 11: SIMPLIS Simulation Philosophy when using Analysis & Control Functions
These features are NOT magic
They are no substitute for understanding
  How your circuit works, and
  How POP works
Better initial conditions are always better
These tools can be very helpful
  For circuits where finding good initial conditions is very difficult
    Variable frequency circuits, like LLCs & Constant ON time controllers
    Initial Conditions for Monte Carlo analyses or Parameter Sweeps where:
      A complex circuit needs to be exercised over a very wide range of operating conditions
18 Sept 2025

## Slide 12: SIMPLIS Essentials Online Short Course
Everything you need to know about
    How POP works, setting Initial Conditions, and
    How to set up POP, AC and Transient analyses
is covered in our SIMPLIS Essentials Online Short Course
  https://www.simplistechnologies.com/training/simplis-essentials
Accessible from our home page
https://simplis.com/
18 Sept 2025